## Slide 10: Pin Layout

## Slide 11
Pin Numbering schemes
Physical Pin
Broadcom Pin Numbering
Wiring-pi
from gpiozero import LED
led =LED(16) # using default numbering scheme : BCM
led =LED(“BCM16”) # using BCM numbering scheme
led =LED(“BOARD36”) # using physical pin numbering
led =LED(“WPI27”) # using physical wiring-pi pin numbering
gpiozero library uses BroadCoM (BCM) pin numbering scheme
By default
Pin Numbering Schemes

## Slide 17
For the hardware configuration, we will first place a resistor of 220 ohms on a breadboard:
Next step is to connect the anode pin of the LED with one leg of the resistor:

## Slide 18: To Light a LED
The long leg of LED is the positive leg, and also called the anode. It should always be connected to the positive side of a circuit. The short leg is the negative leg, called the cathode. It needs to be connected to the negative side.

## Slide 19: Breadboard

## Slide 20
Resistor is connected
to the positive side
Of the LED, in the
Same column

## Slide 21
After connecting anode of LED, we will connect the cathode terminal of the LED with the ground GPIO of Raspberry Pi 4:

## Slide 22
In a final step, connect the 17 GPIO of Raspberry Pi 4 with the open terminal of resistor:

## Slide 23: write the following Python code to control the LED:
import RPi.GPIO as GPIO #include GPIO library
import time # include time library
ledpin = 17 # selecting a pin to be used for connecting LED
GPIO.setwarnings(False) # Disable warnings
GPIO.setmode (GPIO.BOARD) # physical pin numbering scheme is followed
# GPIO.BCM uses BroadCom numbering scheme
GPIO. setup ( ledpin , GPIO.OUT) # selected pin is configured as output
GPIO. output ( ledpin, True) # write high voltage on the led pin
# to turn the LED on
time.sleep (5) # sleep for 5 seconds
GPIO. output ( ledpin, False) # write low voltage on the led pin
# to turn the LED off
GPIO.cleanup() # clear GPIO pins